| GENERAL |
| --- |
| Weigh aircraft for actual weight and balance report |  |  |  |
| Special attention for corrosion of magnesium parts (i.e., control surfaces, castings, etc.) |  |  |  |
| AVIONICS |
| Antenna (requires removal) - corrosion - electrical characteristics |  |  |  |
| Coax cable condition in inaccessible areas |  |  |  |
| Connectors |  |  |  |
| Static dischargers - resistance check |  |  |  |
| Bonding - resistance check |  |  |  |
| ELT - bench check for power output and proper frequency |  |  |  |
| CONTROLS |
| Control surface - balance and rigging |  |  |  |
| Inaccessible areas of control surfaces - corrosion - cracking |  |  |  |
| Attach points - corrosion - cracking |  |  |  |
| Inaccessible control cable runs - condition - corrosion of terminal ends |  |  |  |
| Control surface balance weights - corrosion - security of fasteners - condition of attach points |  |  |  |
| ELECTRICAL |
| Wires (especially inaccessible wiring bundles and wiring behind the control panel) |  |  |  |
| Circuit breakers (check for proper operation at rating) |  |  |  |
| Capacity check of aircraft battery |  |  |  |
| EMPENNAGE |
| Condition of stabilizer attachment structures |  |  |  |
| Inaccessible areas of stabilizers - corrosion - cracking |  |  |  |
| ENGINE |
| Accuracy of engine indicating gauges - tachometer - oil pressure - fuel flow - manifold pressure - exhaust gas temp (EGT) - cylinder head temp (CHT) - oil temperature - fuel pressure |  |  |  |
| Engine mounts - fatigue - cracking - condition of vibration isolators |  |  |  |
| Internal condition of exhaust piping |  |  |  |
| Condition of exhaust clamps and hardware |  |  |  |
| Turbocharge wastegate controller bench - check for proper operation |  |  |  |
| ENGINE (CONTINUED) |
| Accuracy of turbocharger system indicators |  |  |  |
| FUEL SYSTEM |
| Plumbing - rubber hoses |  |  |  |
| Fuel quantity - gauging accuracy |  |  |  |
| Fuel tank installation - corrosion - leakage - plumbing - attachment |  |  |  |
| FUSELAGE |
| Seat tracks - wear - cracking - positive locking of seats |  |  |  |
| Fuselage attach points - wing - stabilizer - landing gear |  |  |  |
| Inaccessible areas (remove all interior items, including headliner, side upholstery panels, carpeting, etc.) - corrosion - cracks |  |  |  |
| INSTRUMENTS |
| Plumbing - condition of rubber hoses |  |  |  |
| Instrument panel shock mounts |  |  |  |
| Pitot/static system - leak check per 91.411 |  |  |  |
| Airspeed/vertical airspeed calibration |  |  |  |
| Altimeter calibration |  |  |  |
| Stall warning system calibration |  |  |  |
| Magnetic compass calibration |  |  |  |
| LANDING GEAR |
| Attach bolts NDT |  |  |  |
| Axle/attach NDT |  |  |  |
| Inaccessible areas of wheel well - corrosion - cracking |  |  |  |
| MODIFICATIONS |
| Records review for proper approval of all modifications including weight and balance revisions |  |  |  |
| Additional continued airworthiness inspection/maintenance requirements for modifications that do not include instructions for continued airworthiness |  |  |  |
| PROPELLER |
| REPAIRS |
| Records review for proper approval of all repairs including weight and balance revisions |  |  |  |
| SYSTEMS |
| Cabin pressure control accuracy |  |  |  |
| Heater muff type heating system - pressure test of exhaust system for leaks |  |  |  |
| Seat belts (certify or replace) |  |  |  |
| Cargo restraints (certify or replace) |  |  |  |
| Fire extinguisher (certify) |  |  |  |
| Hydraulic system plumbing in inaccessible areas |  |  |  |
| Hydraulic system gauging accuracy |  |  |  |
| Proper operation of oxygen regulator |  |  |  |
| Hydrostatic check of oxygen bottle |  |  |  |
| Calibration check of oxygen auto dispensing system |  |  |  |
| Pneumatic plumbing - rubber hoses |  |  |  |
| Pneumatic gauging accuracy |  |  |  |
| SYSTEMS (Continued) |
| Calibration check of pneumatic de-ice system pressure indication (switches or gauges) |  |  |  |
| Vacuum plumbing - rubber hoses |  |  |  |
| Vacuum regulation - accuracy check - proper operation |  |  |  |
| Vacuum gauging accuracy |  |  |  |
| WING |
| Wing attach bolts |  |  |  |
| Strut attach fittings (wood spar) |  |  |  |
| Strut attach fittings (metal spar) |  |  |  |
| Front strut |  |  |  |
| Rear strut |  |  |  |
| Strut attach bolts |  |  |  |
| Spar (metal) |  |  |  |

| WING (Continued) |
| --- |
| Spar (wood) |  |  |  |
| Nails (wood spar) |  |  |  |
| Compression struts |  |  |  |
| Drag wire assembly |  |  |  |
| Ribs/wingtip |  |  |  |
| Fabric |  |  |  |
| Inspection holes |  |  |  |
| Drains |  |  |  |
| Wing general |  |  |  |